2.Aktywacja kierunkowskazów przy otwieraniu i zamykaniu
w E46
Mrugają 2 razy na zamknięcie raz na otwarcie
W końcu wiadomo czy zamknęliśmy samochód
Wszystko analogicznie jak przy światłach do jazdy dziennej :
1 Oczywiście potrzebujemy interfejs do podłączenie się do bmw i program NSC-expert
2 Uruchamiamy NSC musimy stworzyć profil tak więc klikamy File-load profile - expertmode -
OK
następnie File- Edit prifl - hasło: repxet - ok
wybieramy w car/key memory przycisk Individualisierung i zaznaczamy wszystkie 3 opcje
czyli :
individualierung aktiv, kernfunktionen, trace individualizable FSW/PSW - ok
conistance check = sprawdza czy wszystko
klikamy przycisk FSW/PSW i zaznaczamy ptaszkiem FSW/PSW-Manipulate with
FSW_PSW.MAN
OK OK
możemy zapisać ten profil żeby za każdym razem tego nie robić File -save i nazywamy np
E46
3 W katalogu ncsexpert/work utwórz pusty plik FSW_PSW.MAN (np. w notatniku)
4 Kliknij F1 (VIN/ZCS/FA), następnie kliknij F3 (ZCS/FA f.ECU)
5 Wybierz swój samochód w oknie które się otworzy- E46 oczywiście
6 Wybierz ECU do komunikacji, ja wybieram ALSZ
7. Teraz wciśnij F6, czyli Back
8. Wybierz F4 "Program ECU", w tym przypadku kodujemy kierunki, a więc w oknie, które się
pokaże wybieramy moduł GM5
9 Następnie wybieramy F5 (Basic functions) która to funkcja odczytuje nam do pliku
wszystko co mamy w samochodzie zakodowane i następnie w oknie które ci się pokaże
zjedź suwakiem niżej i kliknij dwa razy na „coapireadsggetfswpsw", następuje
odczyt/kopiownaie FSW_PSW.TRC
10 W katalogu ncsexpert/Work znajdziesz teraz plik FSW_PSW.TRC, skopiuj go gdzieś w
inne miejsce na dysku, zmień nazwę na FSW_PSW.MAN, wyedytuj w notatniku i zmień:
DWA
nicht_aktiv
ALARM_OPT_WARNBLINKER
nicht_aktiv
QUIT_OPT_ENTSCH
nicht_aktiv
na
DWA
aktiv
ALARM_OPT_WARNBLINKER
aktiv
QUIT_OPT_ENTSCH
aktiv
11. Następnie po zrobieniu w/w zmian zapisz plik FSW_PSW.MAN i wgraj go do katalogu
ncsexpert/Work, podmieniając wcześniej utworzony.
12 wciskamy Execute Job

Witam, 

Tym razem dokladny opis co sie da i w jakim modelu (do roku 2004). Niestety w language ale zawsze cos. Jezeli dla kogos jest to nieczytelne mam to samo w pdf dokladnie sformatowane: 

Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, R52 and R53 from start of 
series production 
Structure 
1 Car Memory 
1.1 Anti-theft system 
1.2 Central locking system 
1.3 Power windows / sliding/tilt sunroof 
1.4 Lighting 
1.5 Windscreen wipers 
1.6 Cruise control 
1.7 Acoustic warnings 
1.8 Heating / air conditioning / ventilation 
1.9 Seat/mirror memory 
1.10 Displays / language 
1.11 Audio / video 
1.12 Park Distance Control 
2 Key Memory 
2.1 Central locking system 
2.2 Heating / air conditioning / ventilation 
The following overview contains all Car & Key Memory functions that can currently be programmed for series E38, 
E39 vehicles from 09/98 and series E46, E52 and E53 vehicles from start of series production. 
Only Car Memory functions are available for R50/R52/R53 vehicles. 
Functions which do not state a specific model series in the brief description are available for all vehicles capable of 
Car & Key Memory. 
Due to varying legal stipulations, there are national differences in possible settings. Vehicles with the same 
equipment but of a different national variant may have a different range of possible settings. Moreover, the specific 
requirements of vehicle insurance companies in different markets and legal stipulations must be taken into account 
when making settings. 
Factory settings also vary from country to country. 
The vehicle is programmed at the factory in accordance with the central encoding code (ZCS) / vehicle order (VO). 
1.1 Car Memory - Anti-theft system 
Interior movement detector 
o active 
o not active 
The interior movement detector monitoring function can 
be permanently deactivated. This may be advisable if 
animals frequently remain in the vehicle. 
Note insurance requirements! 
E46, E52 - not E38, E39, E53 
Tilt alarm sensor 
o active 
o not active 
The tilt alarm sensor monitoring function can be 
permanently deactivated. This function may be advisable 
if the vehicle is frequently parked in a duplex garage. 
Note insurance requirements! 
E46, E52 - not E38, E39, E53 
Activation/deactivation 
o remote control 
o locks and remote control 
It is only possible to activate/deactivate the anti-theft 
alarm system with the remote control or with the remote 
control and the locks. 
Note insurance requirements in GB, B, NL, F, I - 
deactivation only approved via remote control. 
Not R50, R52, R53 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, BMW AG - TIS 27.08.2009 18:47 
Issue status (02/2004) Valid only until next CD is issued Copyright Page - 1 - 
Confirmation 
Deactivation, optical 
o active 
o not active 
The deactivation of the anti-theft alarm system is 
confirmed by the hazard warning lights flashing briefly. 
Confirmation 
Deactivation, acoustic 
o active 
o not active 
The deactivation of the anti-theft alarm system is 
confirmed by a siren sounding briefly. 
Only permissible on US vehicles. 
Confirmation 
Activation, optical 
o active 
o not active 
The activation of the anti-theft alarm system is confirmed 
by the hazard warning lights flashing briefly. 
Not R50, R52, R53 
Confirmation 
Activation, acoustic 
o active 
o not active 
The activation of the anti-theft alarm system is confirmed 
by a siren sounding briefly. 
Only approved for US vehicles. 
Confirmation 
Activation, optical, doors/hatches closed 
o active 
o not active 
Activation of the anti-theft alarm system is confirmed by a 
brief flashing of the hazard warning lights as soon as all 
doors/hatches are closed. 
E46, E52 - not E38, E39, E53, R50, R52, R53 
Confirmation 
Activation, acoustic, doors/hatches closed 
o active 
o not active 
Activation of the anti-theft alarm system is confirmed by a 
brief siren signal as soon as all doors/hatches are closed. 
Only permitted on US vehicles. 
E46, E52 - not E38, E39, E53, R50, R52, R53 
Confirmation 
Confirmation without anti-theft alarm system 
o active 
o not active 
If "active" is selected, the locking or unlocking of the 
central locking system of a vehicle without anti-theft 
alarm system is verified with an optical or acoustic signal. 
The optical or acoustic signal is dependent on the 
respective national version. 
This setting is effective when the vehicle is locked or 
unlocked either at the lock or with the remote control. 
E38, E39 from 09/99, E46, E53 - not E52, R50, R52, R53 
Please note: 
On E46 vehicles, the fault memory entry "07 
Anti-theft alarm system" is stored in the basic 
module. 
1.2 Car Memory - Central locking system 
Interior lighting, remote control 
o active 
o not active 
The interior lighting is switched on if the car is locked and 
the lock button on the key is pressed. 
If the vehicle is locked a second time within about 15 
seconds, the radio interior movement detector and tilt 
alarm sensor are deactivated. 
Not R50, R52, R53 
Unlock rear window from the inside 
o active 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, BMW AG - TIS 27.08.2009 18:47 
Issue status (02/2004) Valid only until next CD is issued Copyright Page - 2 - 
o not active 
If the setting "active" is selected, the rear window is 
unlocked via a switch in the (driver's side) footwell. If the 
setting "not active" is selected, the rear lid is unlocked. 
E46 Touring 
Remote control, panic mode 
o active 
o not active 
Prolonged pressing of the rear lid release button on the 
key with the anti-theft alarm system activated will trigger 
the alarm in panic mode. 
Not R50, R52, R53 
Open luggage compartment via remote control 
o if unlocked 
o always 
Open the luggage compartment by pressing and holding 
the unlock button. 
E46, E52 - not E38, E39, E53, R50, R52, R53 
Remote control opening mode 
o unlock luggage compartment 
o convenient opening 
o not active 
The rear lid can be unlocked, the windows opened, or no 
function can be set. Operate by remote control with a 
long press of the unlock button on the key. 
R50, R52, R53 
Relock 2 minutes after unlocking if doors are not 
opened 
o active 
o not active 
The vehicle will automatically lock again approx. 2 
minutes after a single inadvertent unlocking (when no 
door or hatch was opened afterwards). 
E38 and E39 from 09/99, E46, E52, E53, R50, R52, R53 
Automatic lock after pulling away 
o active 
o not active 
The vehicle is automatically locked after pulling away. 
Doors can be unlocked at any time from the inside. This 
setting is effective when the doors are mechanically 
opened at the lock. 
For setting to be effective for key with remote control, 
please refer to 2.1 Key Memory - Central locking system. 
Automatic unlocking after engine switch-off 
o active 
o not active 
After switching off the engine, the vehicle is automatically 
unlocked R50, R52, R53. 
Central locking button, when vehicle is locked 
o active 
o not active 
When the vehicle is locked, the driver's and front 
passenger-side doors can be unlocked from the inside by 
pressing the central locking button. The doors can only 
be opened from the inside. The vehicle must first be 
unlocked with the key before it can be locked. Here, it 
makes no difference whether unlocking is carried out 
manually or via remote control. 
If fitted, the anti-theft alarm will be triggered on opening. 
E46, E52 - not E38, E39, E53, R50, R52, R53 
Selective central locking system 
o active 
o not active 
The first time the vehicle is unlocked, only the driver's 
door is unlocked. The remaining doors are not unlocked 
until the vehicle is unlocked a second time. This function 
only applies to manual unlocking via the lock. 
For settings available using the key with remote control, 
see 2.1 Key Memory - central locking system. 
E38, E39, E46, E53, R50, R52, R53 - not E52 
Easy Entry 
Selective central locking 
o active 
o not active 
The Easy Entry facility can be set to active or not active. 
This setting is effective when the vehicle is unlocked 
manually via the lock. 
For the setting to be effective using a key with remote 
control, please refer to 2.1 Key Memory - Central locking 
system. 
Only E46 CoupĂŠ with basic module up to software 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, BMW AG - TIS 27.08.2009 18:47 
Issue status (02/2004) Valid only until next CD is issued Copyright Page - 3 - 
o Easy Entry 
o selective central locking system 
o not active 
Easy Entry facility or selective central locking system can 
be selected. Similarly, both functions can be deactivated. 
This setting is effective when the vehicle is unlocked 
manually via the lock. 
For setting to be effective for key with remote control, 
please refer to 2.1 Key Memory - Central locking system. 
Only E46 CoupĂŠ and R50/R52/R53 
Please note: 
The selection of the setting "Easy Entry" is only 
possible for the E46 CoupĂŠ with basic module 
software version SW1.5 or higher. 
Easy Entry - steering wheel vertical adjustment 
o active 
o not active 
The Easy Entry facility's automatic movement of the 
steering wheel to the upper stop can be set to active or 
not active. 
E53 
Easy Entry - steering wheel longitudinal adjustment 
o active 
o not active 
The Easy Entry facility's automatic movement of the 
steering wheel to the front stop (toward the instrument 
panel) can be set to active or not active 
E53 
Close rear lid with remote control function 
o active 
o not active 
The function to automatically close the rear lid with the 
remote control can be set to active or not active 
E39 Touring 
1.3 Car Memory - Power windows / sliding/tilt sunroof 
Convenient closing, remote control 
o active 
o not active 
Windows and sliding/tilting sunroof can be closed by 
pressing the lock button on the key with remote control - 
apply constant pressure to the "Lock" button. 
E38, E39, E46, E53 - not E46 Convertible, E52, R50, 
R52, R53 
Convenient opening, remote control 
o active 
o not active 
Windows and sliding/tilting sunroof can be opened by 
pressing the unlock button on the key with remote control 
- apply constant pressure to the "Unlock" button. 
E38, E39, E46, E53 - not E46 Convertible, E52, R50, 
R52, R53 
Convenient opening, remote control, without hinged 
windows 
o active 
o not active 
When this setting is active, the hinged windows are not 
opened when convenient opening is effected with the 
remote control. This depends upon the "Remote control 
convenient opening" setting being active. 
E46 CoupĂŠ with basic module from software version 
SW1.5 
Convenient opening lock 
o active 
o not active 
The windows can be opened by operation of the door 
lock - hold the key in the opening position. 
Not R50/R52/R53 
Disable for 
o open door 
o close door 
When "Open door" is selected, the power windows are 
deactivated if terminal R is "off" and the front door is 
open. 
When "Close door" is selected, the power windows are 
deactivated if terminal R is "off" and if, on closing the 
front doors, at least one door was open. 
E38, E39, E53 - not E46, E52, R50, R52, R53 
Close driver's door window, one-touch function 
o active 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, BMW AG - TIS 27.08.2009 18:47 
Issue status (02/2004) Valid only until next CD is issued Copyright Page - 4 - 
o not active 
The driver's door window can be closed by 
pulling/pressing the button beyond the trip point. Use is 
made of the toll function. 
Not R50, R52, R53 
Open driver's door window, one-touch function 
o active 
o not active 
The driver's door window can be opened by pressing the 
button beyond the trip point. Use is made of the toll 
function. 
Not R50, R52, R53 
Close passenger door window, one-touch function 
o active 
o not active 
The passenger door window can be closed by 
pulling/pressing the button beyond the trip point. Use is 
made of the one-touch control function. 
E38, E39, E46, E53 - not E46 Convertible, E52, R50, 
R52, R53 
Open passenger door window, one-touch function 
o active 
o not active 
The passenger door window can be opened by pressing 
the button beyond the trip point. Use is made of the toll 
function. 
Not R50, R52, R53 
Close rear windows, one-touch function 
o active 
o not active 
The rear windows can be closed by pulling/pressing the 
button beyond the trip point. Use is made of the onetouch 
control function. 
E38, E39, E46, E53 - not E46 CoupĂŠ, Convertible, E52, 
R50, R52, R53 
Open rear windows, one-touch function 
o active 
o not active 
The rear windows can be opened by pressing the button 
beyond the trip point. 
Not R50, R52, R53 
Close sliding/tilt sunroof, one-touch function 
o active 
o not active 
The sliding/tilt sunroof can be closed by pressing the 
button to the front. Use is made of the one-touch control 
function. 
Open sliding/tilt sunroof, one-touch function 
o active 
o not active 
The sliding/tilt sunroof can be opened by pressing the 
button to the back. Use is made of the toll function. 
Raise sliding/tilt sunroof, one-touch function 
o active 
o not active 
The sliding/tilt sunroof can be raised by pressing the 
button upwards. Use is made of the one-touch control 
function. 
E38, E46, R50, R52, R53 - not E39, E53 
Open the windows by briefly pressing the central 
button 
o active 
o not active 
The windows can be opened by pressing the central 
switch beyond the trip point. 
E46 Convertible, E52 
1.4 Car Memory - Lighting 
Interior lighting 
ON when unlocking 
o active 
o not active 
The interior lighting is switched on when manual 
unlocking is used. 
E46, E52 - not E38, E39, E53, R50, R52, R53 
Interior lighting 
ON when terminal R is "off", light previously "on" 
o active 
The interior lighting is only switched on when terminal R 
is "off" after driving with lights on. 
E46, E52 - not E38, E39, E53, R50, R52, R53 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, BMW AG - TIS 27.08.2009 18:47 
Issue status (02/2004) Valid only until next CD is issued Copyright Page - 5 - 
Interior lighting 
Soft ON/OFF 
o active 
o not active 
Dimmed interior lighting is switched on and off. 
Not R50, R52, R53 
Exterior lighting 
Daytime driving lights 
o active 
o not active 
The daytime driving lights are switched on as soon as the 
ignition is switched on and the light switch is turned to 
"position 2". 
Note country-specific differences! 
Exterior lighting 
Follow-me-home lights 
o active 
o not active 
If terminal R is "off", the driving lights are switched on for 
the period of time selected when the headlight flasher is 
pulled. The following settings are possible: not active, 
40s, 90s, 150s and 240s. 
(E38, E39, E46, E52, E53, R50, R52, R53). 
For how to activate the function on R50, R53 vehicles, 
please refer to the Owner's Handbook. 
1.5 Car Memory - Windscreen wipers 
Rain sensor 
o active 
o not active 
The rain sensor can be deactivated. 
E46 - not E38, E39, E52, E53, R50, R52, R53 
Switch down when stationary 
o active 
o not active 
The system switches from speed 1 to intermittent 
operation or from speed 2 to speed 1 when the vehicle is 
stationary. 
Rain-light sensor 
o sensitive 
o less sensitive 
The response of the rain-light sensor can be adjusted to 
be sensitive or less sensitive. 
E39, E46, E53, not R50, R52, R53 
1.6 Car Memory - Cruise control 
Activate 
o active 
o not active 
The cruise control can be activated either via a switch on 
the instrument mount or via the button on the multifunction 
steering wheel. 
E38, E39 with switch on instrument mount 
Active Cruise Control (ACC) desired speed 
o current 
o rounded 
If the setting "current" is selected, the current speed is 
adopted as the desired speed the first time the ACC is 
activated with the set/accelerate button. The display is 
made with the next-higher LED. If the setting "rounded" is 
selected, the speed of the vehicle when the ACC is 
activated is rounded up to the next multiple of 10 km/h or 
5 mph and adopted as the desired speed. 
E38 with ACC 
1.7 Car Memory - Acoustic warnings 
Ignition key 
o active 
o not active 
If the ignition key is still in the ignition lock when the 
driver's door is open, an acoustic signal will sound. 
This function is advisable if children are occasionally left 
in the vehicle who are able to play with the ignition key. 
Fuel tank warning 
o active 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, BMW AG - TIS 27.08.2009 18:47 
Issue status (02/2004) Valid only until next CD is issued Copyright Page - 6 - 
o not active 
If the fuel tank reserve indicator lamp lights up, an 
acoustic signal sounds. 
R50, R52/R53 only 
1.8 Car Memory - Heating / air conditioning / ventilation 
Key selective 
o active 
o not active 
The Key Memory can be activated or deactivated for the 
air-conditioning system. Using the "active" setting, 
temperature and blower settings, and air conditioning 
functions (AUC, air recirculation, flaps, defrost) are stored 
for each key individually. 
E39, E53 - not E38, E46, E52, R50, R52, R53 
Flaps 
Air recirculation flaps memory 
o active 
o not active 
Air recirculation is retained after restarting the engine. 
The function is not dependent on the key used. 
E38, E39, E46, E53 - not E52, R50, R52, R53 
Cooling output 
o normal 
o hot country 
The air conditioner control can be set to normal or as per 
hot country variant. If the hot country setting is selected, 
more cooling output is available due to appropriate 
blower output and flap control. 
E38, E39, E46 - not E52, E53, R50, R52, R53 
Automatic heated rear window 
o active 
o not active 
The function to automatically switch the heated rear 
window on at an ambient temperature of less than 3.5 
degrees Celsius can be set to active or not active. 
E46 
1.9 Car Memory - Seat/mirror memory 
Seat position 
o when car is unlocked 
o when door is opened 
o not active 
The seat is moved to the stored position when the vehicle 
is unlocked using the key with remote control or after the 
driver's door is opened. A key-specific seat adjustment is 
not possible if "not active" is selected. 
On E38, E39 and E53 vehicles, not only the seat but also 
the mirrors and the steering column (if the latter can be 
electrically adjusted) change their positions. 
On E46 vehicles, the mirrors are adjusted on vehicles 
from production period 09/99 (Model Year 00). 
Please note: 
Seat positioning is interrupted by pressing the 
lock button on the key with remote control. 
E38, E39, E46, E53 - not E52, R50, R52, R53 
Mirror memory - Automatic parking function 
o active 
o not active 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, BMW AG - TIS 27.08.2009 18:47 
Issue status (02/2004) Valid only until next CD is issued Copyright Page - 7 - 
The position of the passenger-side exterior mirror for the 
automatic parking function can be stored for each key 
individually. 
If "active" is selected and the mirror adjustment switch 
set to "passenger-side mirror", the passenger-side mirror 
will automatically be moved to the key-specific position 
when reverse gear is engaged. 
If "active" is selected and the mirror adjustment switch 
set to "driver's-side mirror", the automatic parking 
function is deactivated. 
If "not active" is selected and the mirror adjustment 
switch set to "driver's-side mirror", the passenger-side 
mirror is automatically adjusted to the lowest possible 
position when reverse gear is engaged. 
If "not active" is selected and the mirror adjustment 
switch set to "passenger-side mirror", the automatic 
parking function is deactivated. 
E46 from 09/99 
Exterior mirror automatic parking function with LIN 
connection 
o active 
o not active 
A LIN bus is installed on the E46 from 03/03. When the 
system is "active" and the mirror-adjustment switch is 
moved to the "passenger-side mirror" position, the mirror 
on the passenger's side is lowered when reverse gear is 
engaged. To enable a key-specific setting to be made, 
the function "Folding mirror down" must also be 
activated. 
E46 only 
Exterior mirror automatic parking function memory 
with LIN connection 
o active 
o not active 
A LIN bus is installed on the E46 from 03/03. When the 
system is "active", different key-specific angles for folding 
down can be set for the automatic parking function. 
E46 only 
Automatic mirror adjustment 
o active 
o not active 
A LIN bus is installed on the E46 from 03/03. When the 
system is "active", the mirrors are automatically set 
according to the key used when the vehicle is unlocked 
with the radio remote control. This function must be set 
separately from the automatic seat adjustment. 
E46 only 
1.10 Car Memory - Displays / language 
Units 
Fuel consumption 
o litres/100 km 
o mpg (UK) 
o mpg (US) 
o km/litre 
After setting the following functions, the clock must be 
reset to the correct time. 
Fuel consumption can be displayed in the given units. 
E38, E39, E46, E53, R50, R52, R53 without on-board 
monitor - not E52 
Units 
Distance 
o km 
o miles 
Distance covered can be indicated in the units given. 
E38, E39, E46, E52, E53 without on-board monitor 
R50, R52, R53 
Units 
Time 
o 12 h 
o 24 h 
The clock can be set in the given modes. 
E38, E39, E46, E53, R50, R52, R53 without on-board 
monitor - not E52 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, BMW AG - TIS 27.08.2009 18:47 
Issue status (02/2004) Valid only until next CD is issued Copyright Page - 8 - 
o degrees F 
The ambient temperature can be displayed in the given 
units. 
E38, E39, E46, E53, R50, R52, R53 without on-board 
monitor - not E52 
Language 
Text display 
o German 
o English 
o Italian 
o Spanish 
o Japanese 
o French 
o Gulf states 
The display texts can be displayed in the given 
languages. 
E38, E39, E53 without on-board monitor - not E46, E52, 
R50, R52, R53 
Basic settings 
Temporary ice warning 
o active 
o not active 
The ice warning can be set to active or not active. 
Active: If the ambient temperature drops below about + 3 
(C, the acoustic ice warning sounds and the ambient 
temperature display flashes for a few seconds. The 
display then reverts to the previous display unit. 
Not active: If the ambient temperature drops below about 
+ 3(C, the acoustic ice warning sounds. The outside 
temperature is then permanently displayed. By pressing 
the steering column switch a different display unit is 
obtained. 
E46 with instrument cluster from software version SW11 - 
R50, R52, R53, not E38, E39, E52, E53 
1.11 Car Memory - Audio / video 
Basic telephone interface - mobile phone type 
o Nokia 3110 
o Siemens S10 
Mobile phone type can be changed in the case of a 
conversion or retrofit. 
E46 - not E38, E39, E52, E53, R50, R52, R53 
Please note: 
The mobile phone type must be set when 
retrofitting the basic telephone interface with 
"Encoding ZCS - Retrofit". 
New generation radio - key selective 
o active 
o not active 
The Key Memory can be activated or deactivated for the 
radio. With the "active" setting, the sound, the last audio 
source selected (radio, cassette, CD) and the last radio 
station tuned are stored for each key individually. 
E39, E46, E53 with New Generation Radio - not E38, 
E52, R50, R52, R53 
GAL-TCUI 
o 30 km/h 
o 48 km/h 
o 56 km/h 
Speed threshold for raising volume. 
E46 US only 
1.12 Car Memory - Park Distance Control 
Signal volume, rear 
o level 1 (quiet) 
o Level 2 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, BMW AG - TIS 27.08.2009 18:47 
Issue status (02/2004) Valid only until next CD is issued Copyright Page - 9 - 
o level 5 
o level 6 (loud) 
The volume of the acoustic signal can be adjusted. 
Volume at level 1: quiet 
Volume at level 6: loud 
E38 and E39 from 09/99, E53, R50, R52, R53 - not E46, 
E52 
Rear activation confirmation 
o active 
o not active 
An acoustic signal sounds when reverse gear is engaged 
(PDC activation). 
E39, E46, R50, R52, R53 - not E38, E52, E53 
2.1 Key Memory - Central locking system 
Automatic lock after pulling away 
o active 
o not active 
The vehicle is automatically locked when it pulls away. It 
is still possible to open it from the inside. This function is 
effective when the doors are opened using the remote 
control. 
For the setting to be effective using a key at the lock, 
please refer to 1.2 Car Memory - Central locking system. 
Radio unlocking 
o rear window 
o rear lid 
Open the rear lid or rear window with remote control by 
pressing the button on the key. 
E46 Touring 
Selective central locking system 
o active 
o not active 
The first time the button on the key is pressed, only the 
driver's door is unlocked. If it is pressed a second time, 
the whole car is opened. This function is only effective 
when the remote control is used. 
For the setting to be effective using a key at the lock, 
please refer to 1.2 Car Memory - Central locking system. 
E38, E39, E46, E53 - not E52, R50, R52, R53 
Easy Entry 
o active 
o not active 
The Easy Entry facility can be set to active or not active. 
This setting is effective when the vehicle is unlocked 
with the remote control. 
For the setting to be effective using a key at the lock, see 
section 1.2 Key Memory - Central locking system. 
Only E46 CoupĂŠ with general module up to software 
version SW1.4 
Easy Entry / selective central locking 
o Easy Entry 
o selective central locking system 
o not active 
Easy Entry or selective central locking can be selected. 
Similarly, both functions can be deactivated. This setting 
is effective when the vehicle is unlocked with the 
remote control. 
For the setting to be effective using a key at the lock, see 
section 1.2 Car Memory - Central locking system. 
Only E46 CoupĂŠ 
Please note: 
The selection of the setting "Easy Entry" is only 
possible for the E46 CoupĂŠ with basic module 
software version SW1.5 or higher. 
2.2 Key Memory - Heating / air conditioning / ventilation 
Blower 
Setting blower speed 
In automatic operation, the normal blower output can be 
increased or decreased 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50, BMW AG - TIS 27.08.2009 18:47 
Issue status (02/2004) Valid only until next CD is issued Copyright Page - 10 - 
Blower 
Air conditioning auto mode 
o active 
o not active 
When this function is active, air-conditioning automatic 
mode is started when the ignition is switched on. 
E46 only 
Vent flaps 
Ventilation open in warming-up phase 
o yes 
o no 
During the warming-up phase, the ventilation flaps are 
open or closed. 
E46 - not E38, E39, E52, E53, R50, R52, R53 
Vent flaps 
After terminal 15 "ON" 
o yes 
o no 
Manual control of the ventilation flaps using the 3 buttons 
on the air conditioning control panel can be activated 
directly by switching on the ignition. 
E46 - not E38, E39, E52, E53, R50, R52, R53 
Vent flaps 
Correction of specified temperature 
o + 3 degrees 
o + 2 degrees 
o + 1 degree 
o not active 
o - 1 degree 
o - 2 degrees 
o - 3 degrees 
The set temperature in the display can be corrected 
accordingly. 
E46 - not E38, E39, E52, E53, R50, R52, R53 
Vent flaps 
Air conditioner ON 
o if ignition on 
o with button only 
The air conditioning system will start operating when the 
ignition is switched on or only by pressing the button on 
the air conditioning control panel. 
E46 - not E38, E39, E52, E53, R50, R52, R53 
Vent flaps 
Automatic blower 
o active 
o not active 
The automatic blower will start operating when the 
ignition is switched on or only by pressing the button on 
the air conditioning control panel. 
E46 - not E38, E39, E52, E53, R50, R52, R53 
IDC Car & Key Memory functions for series E38, E39 (from 09/98), E46, E52, E53, R50,